## Slide 1: Instruction Set Principles
(Appendix B)

## Slide 2: Instruction Set Architecture (ISA)
S o f t w a r e
Hardware
i n s t r u c t i o n s e t

## Slide 3: Interface Design (ISA)
A good interface:
  Lasts through many implementations (portability, compatibility)
  Is used in many different ways (generality)
  Provides convenient functionality to higher levels
  Permits an efficient implementation at lower levels
Interface
imp 1
imp 2
imp 3
use
use
use
time
I S A

## Slide 4: Classification of ISAs
Stack Architecture
  Only data structure: Stack
Accumulator Architecture
  Only one register: Accumulator
General Purpose Register (GPR) Architecture
  Set or Registers (Register File)
  3 sub-architectures:
    Reg-Reg (Load/Store)
    Reg-Mem or Mem-Reg
    Mem-Mem

## Slide 5: Operand location for ISAs

## Slide 6: Example: MIPS
0
r0
r1
°
°
°
r31
PC
lo
hi
Programmable storage
2^32 x bytes
31 x 32-bit GPRs (R0=0)
32 x 32-bit FP regs (paired DP)
HI, LO, PC
  Arithmetic logical
  Add, AddU, Sub, SubU, And, Or, Xor, Nor, SLT, SLTU,
  AddI, AddIU, SLTI, SLTIU, AndI, OrI, XorI, LUI
  SLL, SRL, SRA, SLLV, SRLV, SRAV
  Memory Access
  LB, LBU, LH, LHU, LW,
  SB, SH, SW,
  Control
  J, JAL, JR, JALR
  BEq, BNE, BLEZ,BGTZ,BLTZ,BGEZ,BLTZAL,BGEZAL
32-bit instructions on word boundary
unsigned
immediate
Set Less Than
Shift left logical
Shift right arithm.

## Slide 7: CISC vs. RISC
First computers were RISC
Cray supercomputers were RISC
Complexity was added in the 70s and 80s
Return to simplicity in 80’s and 90’s

## Slide 8: Why Return to RISC?
CISC provides too many possibilities
Compilers can’t choose optimal encoding
70 instructions = 99% of code
50 instructions = 95% of code

## Slide 9: Why Did CISC Happen?
Fetch- Execute cycle
Limited memory
Reduce fetches and memory by packing multiple ops into each instruction
Observe common sequences of ops and turn them into instructions

## Slide 10: CISC Features
Memory accesses and address arithmetic are tightly bound to instructions
Rely on few registers, more memory references
Note that memory hasn’t kept pace with processor clock rate

## Slide 11: Reduced Instruction Set Computers (Cocke, IBM; Patterson, UC Berkeley; Hennessy, Stanford)
Compilers have difficulty using complex instructions
VAX: 60% of microcode for 20% of instructions, only responsible for 0.2% execution time
IBM retargets 370 compiler to use ISA subset - generated code faster!
Simple instruction sets do not need microcode
Use fast memory near processor as cache, not microcode storage
Design ISA for simple pipelined implementation
  Fixed length, fixed format instructions
  Load/store architecture with up to one memory access/instruction
  Few addressing modes, synthesize others with code sequence
  Register-register ALU operations
  Delayed branch

## Slide 12: Benefits of RISC
Reduced CPI (cycles per instruction)
Reduced decoding delay
Simpler core design enables more chip area to be used for performance
But today, CISC architectures like Intel use a RISC core for a subset of instructions
Why are RISC designs still faster?

## Slide 13: Code Expansion
RISC does less with each instruction
Large code size (1.3 to 1.6 X)
Larger number of memory fetches
Partly alleviated by larger cache
Still generates more memory traffic than CISC
Compressed instruction blocks?

## Slide 14: Common RISC Features
Load/ Store designs
Few addressing modes
Fixed instruction size
Few instruction formats
Few operand sizes
Use more registers, separate memory operations

## Slide 15: MIPS R2000 (One of first commercial RISCs, 1986)
Load/Store architecture
  32x32-bit GPR (R0 is wired), HI & LO SPR (for multiply/divide)
  74 instructions
  Fixed instruction size (32 bits), only 3 formats
  PC-relative branches, register indirect jumps
  Only base+displacement addressing mode
  No condition bits, compares write GPRs, branches test GPRs
  Delayed loads and branches
Five-stage instruction pipeline
  Fetch, Decode, Execute, Memory, Write Back
  CPI of 1 for register-to-register ALU instructions
  8 MHz clock
  Tightly-coupled off-chip FP accelerator (R2010)

## Slide 16: RISC/CISC Comparisons
R2000 vs VAX 8700 [Bhandarkar and Clark, ‘91]
R2000 has ~2.7x advantage with equivalent technology
Intel 80486 vs Intel i860 (both 1989)
Same company, same CAD tools, same process
i860 2-4x faster - even more on some floating-point tasks
DEC nVAX vs Alpha 21064 (both 1992)
  Same company, same CAD tools, same process
  Alpha 2-4x faster

## Slide 17: A "Typical" RISC
32-bit fixed format instruction (3 formats)
32 32-bit GPR (R0 contains zero, DP take pair)
3-address, reg-reg arithmetic instruction
Single address mode for load/store: base + displacement
  no indirection
Simple branch conditions
Delayed branch
See: SPARC, MIPS, HP PA-Risc, DEC Alpha, IBM PowerPC,
CDC 6600, CDC 7600, Cray-1, Cray-2, Cray-3

## Slide 18: Example: MIPS
Op
31
26
0
15
16
20
21
25
Rs1
Rd
immediate
Op
31
26
0
25
Op
31
26
0
15
16
20
21
25
Rs1
Rs2
target
Rd
Opx
Register-Register
5
6
10
11
Register-Immediate
Op
31
26
0
15
16
20
21
25
Rs1
Rs2/Opx
immediate
Branch
Jump / Call