## Slide 1: Critical Infrastructure Security: The Emerging Smart Grid In Class: Cpt S 580-03, Cpt S 483-01, EE 582-02, EE 483-01 Online or Tri-Cities: Cpt S 580-03, Cpt S 483-01, Cpt S 483-02, EE 582-01, EE 483-01
Dr. Anurag K. Srivastava, Dr. Carl Hauser, Dr. Dave Bakken,
and Dr. Min Sik Kim
Computation Lecture 3: Overview of Fault-Tolerant Computing

## Slide 2: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 3: Administrivia
Email about midterm
Hand back first assignment

## Slide 4: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 5: A Definition of Dependability (6.1)
Dependability deals with having a high probability of behaving according to specification (informal definition)
Implications
  Need a comprehensive specification
  Need to specify not only functionality but assumed environmental conditions
  Need to clarify what “high” means (context-dependent)

## Slide 6: Defining Dependability (cont.)
Dependability: the measure in which reliance can justifiably be placed on the service delivered by a system
  Q: what issues does this definition raise?
Is there a systematic way to achieve such justifiable reliance?
  No silver bullets: fault tolerance is an art
  Prereq #1: know impairments to dependablity
  Prereq #2: know means to achieve dependability
  Prereq #3: devise ways of specifying/expressing level of dependability required
  Prereq #4: measure if it the required level of dependability was achieved

## Slide 7: Faults,Errors, and Failures
Some definitions from the fault tolerance realm
  Fault: the adjudged (hypothesized) cause for an error
  Note: may lie dormant for some time
    Running Example: file system disk defect or overwriting
    Example: software bug
    Example: if a man talks in the woods…..
  Error: incorrect system state
    Running Example: wrong bytes on disk for a given record
  Failure: component no longer meets its specification
    I.e., the problem is visible outside the component
    Running Example: file system API returns the wrong byte
Sequence (for a given component):
  Fault Error  Failure

## Slide 8: Cascading Faults,Errors, and Failures
Can cascade (if not handled)
  Scenario: Component 2 uses Component 1
  Lets see if you can get the terms right..
Component1
Component2
This is ….
This is ….
This is …. (of Component1)
This is …. (to Component2)
Fault
Error
Failure
Fault
1
1
1
0
1
1
1
1

## Slide 9: Fault Types
Several axes/viewpoints by which to classify faults…
Phenomenological origin
  Physical: HW causes
  Design: introduced in the design phase
  Interaction: occuring at interfaces between components
Nature
  Accidental
  Intentional/malicious
Phase of creation in system lifecycle
  Development
  Operations
Locus (external or internal)
Persistence (permanent or temporary)

## Slide 10: More on Faults
Independent faults: attributed to different causes
Related faults: attributed to a common cause
Related faults usually cause common-mode failures
  Single power supply for multiple CPUs
  Single clock
  Single specification used for design diversity

## Slide 11: Scope of Fault Classification
NATURE
ORIGIN
PERSISTENCE
Phenomenological
Cause
System Boundaries
Phase of Creation
Usual
Labelling
Physical Faults
Transient Faults
Intermittent
Faults
Design Faults
Interaction Faults
Malicious
Logic
Intrusions
Accidental
Faults
Intentional
Faults
Physical
Faults
Human-made
Faults
Internal
Faults
External
Faults
Design
Faults
Operational
Faults
Permanent
Faults
Temporary
Faults
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X
X

## Slide 12: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 13: Achieving Dependability (6.1 B)
Chain of failures likely to cascade unless handled!
  To get dependability, break that chain somewhere!
Fault removal: detecting and removing faults before they can cause an error
  Find software bugs, bad hardware components, etc.
Fault forecasting: estimating the probability of faults occuring or remaining in system
  Can’t remove all kinds easily/cheaply!
Fault prevention: preventing causes of errors
  Eliminate conditions that make fault occurrence probable during operation
    Use quality components
    Use components with internal redundancy
    Rigorous design techniques
Fault avoidance: fault prevention + fault removal

## Slide 14: Achieving Dependability (cont.)
Can’t always avoid faults, so better tolerate them!
Fault-Tolerant System: a system that can provide service despite one or more faults occurring
  Acts at the phase that errors are produced (operation)
Error detection: finding the error in the first place
Error processing: mechanisms that remove errors from computational state (hopefully before failure!)
2 Choices:
  Error recovery: substitute an error-free state for the erroneous one
    Backward recovery: go back to a previous error-free state
    Forward recovery: find a new state system can operate from
  Error compensation: erroneous state contains enough redundancy to enable delivery of error-free service from the erroneous state

## Slide 15: Achieving Dependability (cont.)
Fault Treatment: preventing faults from re-occuring
Steps:
  Fault diagnosis: determining cause(s) of the error(s)
  Fault passivation: preventing fault(s) from being activated again
    Remove component
    If can’t continue with this removed, need to reconfigure system

## Slide 16: Measuring and Validating Dependability
We’ve practiced fault avoidance & fault tolerance….
  But how good did we do???
  Attributes by which we measure and validate dependability…
Reliability: probability that system does not fail during a given time period (e.g., mission or flight)
  Mean time between failures (MTBF): useful for continuous mission systems (a scalar)
  Other quantifications are
    probability distribution functions (e.g., bathtub)
    Scalar: failures per hour (e.g., 10-9)
Maintainability: measure of time to restore correct service
  Mean time to repair (MTTR): a scalar measure

## Slide 17: Measuring & Validating Dependability (cont).
Availability: prob. a service is correctly functioning when needed (note: many sub-definitions…)
  Steady-state availability: the fraction of time that a service is correctly functioning
    MTBF/(MTBF+MTTR)
  Interval availability (one explanation): the probability that a service will be correctly functioning during a time interval
    E.g., during the assumed time for a client-server request-reply
Performability: combined performance+dependability analysis
  Quantifies how a system gracefully degrades
Safety: degree that system failing is not catastrophic
Security ≅ Confidentiality∧Integrity∧Availability
Note: dependability measures vary w/ resources+usage

## Slide 18: Availability Examples
Availability | 9s | Downtime/year | Example Component
90% | 1 | >1 month | Unattended PC
99% | 2 | ~4 days | Maintained PC
99.9% | 3 | ~9 hours | Cluster
99.99% | 4 | ~1 hour | Multicomputer
99.999% | 5 | ~5 minutes | Embedded System (w/PC technology)
99.9999% | 6 | ~30 seconds | Embedded System (custom HW)
99.99997% | 7 | ~3 seconds | Embedded System (custom HW)

## Slide 19: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 20: Fault Assumptions
Can’t design to tolerate an arbitrary number and kind of faults! (IMHO; YMMV.)
Fault model: number of classes of faults that have to be tolerated
  AKA failure model (failure of a component being used)
  2 main groupings of fault model: omissive and assertive
  In this segment we mainly deal with interaction faults
    Q: why?
Fault model done at atomic level of abstraction not possible or useful to go below
  Nicely groups lower-level problems at the granularity that you would want to do something about it!

## Slide 21: Omissive Fault Group
Omissive faults: component not performing an interaction it was specified to
  Crash: component permanently (but cleanly) stops
    AKA “fail silent”
  Omission: component periodically omits a specified interaction
    Omisssion degree: # of successive omission faults
    Note crash is an extreme case of omission: infinite omission degree
  Timing: component is later (or earlier) than performing specified interaction
    Note: omission is extreme case of timing fault: infinite lateness

## Slide 22: Assertive and Arbitrary Faults
Assertive faults: interactions not performed to spec.
  Syntactic: wrong structure of interaction
    E.g., sending a float instead of an int
  Semantic: wrong meaning
    E.g., bad value
    E.g., temp sensor below absolute zero
    E.g., Sensor very different from redundant sensors
Arbitrary faults: union of omissive and assertive
  Note: omissive faults occur in the time domain
  Note: assertive faults occur in the value domain
  Arbitrary can be either

## Slide 23: Arbitrary Faults (cont.)
Causes of arbitrary faults
  Improbable but possible sequence of events
  A bug
  Deliberate action by intruder
Byzantine faults: subset of arbitrary
  Generally defined as sending bad values and often inconsistent semantic faults (“two-faced behavior”)
  One counter-example sub-case: a malicious early timing fault
    Really a forged interaction
    Non-malicious early timing fault happened to my lab machines in fall 2000…

## Slide 24: Summary: Classes of Interaction Faults
Caveat: it’s a Byzantine (and Machievellian) world out there….
“You've got to ask yourself one question. Do you feel lucky? Well, do you... Punk”
Caveat: it’s a Byzantine (and Machievellian) world out there….
“You've got to ask yourself one question. Do you feel lucky? Well, do you... Punk”

## Slide 25: Coverage
To build a FT system you had to assume a fault model
  But how good (lucky?) were you in you assumptions???
Q: which is “better”
  A system tolerating two arbitrary faults
  A system tolerating two omission faults
  A system tolerating one omission and one arbitrary fault
Coverage: given a fault, it’s the probability that it will be tolerated
Assumption coverage (informally): the probability that the fault model will not be violated

## Slide 26: Causes of Failures
Jim Gray (RIP) survey at Tandem (1986)
  Still relevant today
Causes of failures (“How do computers fail…”)
  Plurality (42%) caused by incorrect system administration or human operators
  Second (25%) software faults
  Third: environmental (mainly power outage, but flood/fire)
  Last: hardware faults
Lessons for the system architect (“…and what can be done about it?”)
  Dependability can be increased by careful admin/ops
  SWE methodologies that help with fault prevention and removal can significantly increase reliability
  Software fault tolerance is a very critical aspect

## Slide 27: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 28: Fault-Tolerant Computing (6.2)
Recall: FT computing is techniques that prevent faults from becoming failures
  Quite a span of mechanisms…
FT requires some kind(s) of redundancy (examples?)
  Space redundancy: having multiple copies of a component
  Time redundancy: doing the same thing more than once until desired effect achieved
    Can be redone same way or different way
  Value redundancy: adding extra information about the value of the data being stored/sent

## Slide 29: Error Processing
Facets of error processing
  Error detection: discovering the error
  Error recovery: utilize enough redundancy to keep operating correctly despite the error
    Backward error recovery: system goes back to a previous state known to be correct
    Forward error recovery: system proceeds forward to a state where correct provision of service can still be ensured
      Usually in a degraded mode
  Error masking: providing correct service despite lingering errors
    AKA error compensation
    E.g., receiving replies from multiple servers and voting
    E.g, sending three identical messages and voting

## Slide 30: Distributed Fault Tolerance (DFT)
Modularity is important for FT
DFT sys. built of nodes, networks, SW components
  Key goal: decouple SW components from HW they run on
  This modularity greatly helps reconfiguration and replication

## Slide 31: Distributed Fault Tolerance (cont.)
If right design techniques used, you can replace HW or SW components without changing the arch.
Also lets you provide incremental dependability
  Adding more replicas
  Hardening fragile ones (fault prevention)
  Making more resilient to severe faults (fault tolerance)
Can also support graceful degradation: system does not collapse quickly at some point, service provided at lower level
  Slower
  Less precise results
Modularity also helps support heterogeneity
  Usually with distributed object middleware

## Slide 32: Today’s Content
Administrivia
A Definition of Dependability (6.1)
  Basic Definitions
  Achieving, Measuring, and Validating Dependability
  Fault Assumptions
Fault-Tolerant Computing (6.2)
Fault-Tolerant Architectures (6.5)

## Slide 33: Fault-Tolerant Architectures (6.5)
Give some examples now of FT, details later
Approaches increasing local availability for crashes
  (a) redundant storage (RAID)
  (b) redundant processors

## Slide 34: FT Architectures (cont.)
Tolerating crashes OK, tol. misbehavior better….
Redundant Architectural Models:
  (a) Self-Checking: checker detects an error and halts
  (b) N-Modular Redundancy(NMR): lock-step CPUs and instruction-by-instruction comparison
    Tolerates up to (but not including) half of the CPUs failing
Caveat: “But who will guard the guards?” Caesar

## Slide 35: FT Architectures (cont.)
Local is nice, but remote is better…..
  Lock-step too constraining and inefficient
    Let them execute at same logical time, not physical time
    Geographic dispersion for more fault independence
Distributed replication architectures: replica groups communicate among themselves (lots of ways…)