## Slide 1
Lab 2
  Late
  No Videos
Lab 3
  Late
  Write up
  Functions
  150cm spiral
Homework
Labs 4-6
Final Project

## Slide 2: Mid-semester feedback
What do you think of the balance of theoretical vs. applied work?
What’s been most useful to you (and why)?
What’s been least useful (and why)?
What could students do to improve the class?
What could Matt do to improve the class?

## Slide 3: Example
Right

## Slide 4: Kalman Filter (Section 5.6.8)
Sense
Move
Initial Belief
Gaussian:
μ, σ2
μ’=μ+u
σ2’=σ2+r2

## Slide 5: Kalman Filter in Multiple Dimensions
2D Gaussian

## Slide 6: Implementing a Kalman Filter example
VERY simple model of robot movement:
What information do our sensors give us?

## Slide 7: Implementing a Kalman Filter example
H = [1 0]
F
H

## Slide 8: Implementing a Kalman Filter
Estimate
P’ uncertainty covariance
F state transition matrix
u motion vector
F motion noise
Measurement
measurement function
measurement noise
identity matrix

## Slide 9: Particle Filter Localization (using sonar)
http://www.cs.washington.edu/ai/Mobile_Robotics//mcl/animations/global-floor-start.gif

## Slide 10: Particles
Each particle is a guess about where the robot might be
x
y
θ

## Slide 11: Robot Motion
move each particle according to the rules of motion
+
add random noise
particles
particles

## Slide 12: Incorporating Sensing

## Slide 13: Incorporating Sensing

## Slide 14: Incorporating Sensing
Difference between the
actual measurement
and the
estimated measurement
Importance weight

## Slide 15: Importance weight python code
def Gaussian(self, mu, sigma, x):
# calculates the probability of x for 1-dim Gaussian with mean mu and var. sigma
return exp(- ((mu - x) ** 2) / (sigma ** 2) / 2.0) / sqrt(2.0 * pi * (sigma ** 2))
def measurement_prob(self, measurement):
# calculates how likely a measurement should be
prob = 1.0;
for i in range(len(landmarks)):
dist = sqrt((self.x - landmarks[i][0]) ** 2 + (self.y - landmarks[i][1]) ** 2)
prob *= self.Gaussian(dist, self.sense_noise, measurement[i])
return prob
def get_weights(self):
w = []
for i in range(N): #for each particle
w.append(p[i].measurement_prob(Z)) #set it’s weight to p(measurement Z)
return w

## Slide 16: Importance weight pseudocode
Calculate the probability of a sensor measurement for a particle:
prob = 1.0;
for each landmark
d = Euclidean distance to landmark
prob *= Gaussian probability of obtaining a reading at
distance d for this landmark from this particle
return prob

## Slide 17: Incorporating Sensing

## Slide 18: Resampling
original particles
Importance Weight |  | 
0.2 |  | 
0.6 |  | 
0.2 |  | 
0.8 |  | 
0.8 |  | 
0.2 |  | 
Sum is 2.8

## Slide 19: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8

## Slide 20: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement

## Slide 21: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
Is it possible that one of the particles is never chosen?
Yes!
Is it possible that one of the particles is chosen more than once?
Yes!

## Slide 22: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
What is the probability that this particle is not chosen during the resampling of the six new particles?
Notes: .71 ^ 6 = 12.8%

## Slide 23: Resampling
original particles
Importance Weight | Normalized Probability | 
0.2 | 0.07 | 
0.6 | 0.21 | 
0.2 | 0.07 | 
0.8 | 0.29 | 
0.8 | 0.29 | 
0.2 | 0.07 | 
Sum is 2.8
Sample n new particles from previous set
Each particle chosen with probability p, with replacement
What is the probability that this particle is not chosen during the resampling of the six new particles?

## Slide 24: Question
What happens if there are no particles near the correct robot location?

## Slide 25: Question
What happens if there are no particles near the correct robot location?
Possible solutions:
  Add random points each cycle
  Add random points each cycle, where is proportional to the average measurement error
  Add points each cycle, located in states with a high likelihood for the current observations

## Slide 26: Summary
Kalman Filter
  Continuous
  Unimodal
  Harder to implement
  More efficient
  Requires a good starting guess of robot location
Particle Filter
  Continuous
  Multimodal
  Easier to implement
  Less efficient
  Does not require an accurate prior estimate

## Slide 27: SLAM
Simultaneous localization and mapping:
    Is it possible for a mobile robot to be placed at an unknown location in an unknown environment and for the robot to incrementally build a consistent map of this environment while simultaneously determining its location within this map?
http://flic.kr/p/9jdHrL

## Slide 28: Three Basic Steps
The robot moves
  increases the uncertainty on robot pose
  need a mathematical model for the motion
  called motion model

## Slide 29: Three Basic Steps
The robot discovers interesting features in the environment
  called landmarks
  uncertainty in the location of landmarks
  need a mathematical model to determine the position of the landmarks from sensor data
  called inverse observation model

## Slide 30: Three Basic Steps
The robot observes previously mapped landmarks
  uses them to correct both self localization and the localization of all landmarks in space
  uncertainties decrease
  need a model to predict the measurement from predicted landmark location and robot localization
  called direct observation model

## Slide 31: How to do SLAM

## Slide 32: How to do SLAM

## Slide 33: How to do SLAM

## Slide 34: How to do SLAM

## Slide 35: How to do SLAM

## Slide 36: How to do SLAM

## Slide 37: How to do SLAM

## Slide 38: How to do SLAM

## Slide 39: How to do SLAM

## Slide 40: The Essential SLAM Problem

## Slide 41: SLAM Paradigms
Some of the most important approaches to SLAM:
  Extended Kalman Filter SLAM (EKF SLAM)
  Particle Filter SLAM (FAST SLAM)
  GraphSLAM

## Slide 42: EKF Slam
Keep track of combined state vector at time t:
  x, y, θ
  m1,x, m1,y, s1
  …
  mN,x, mN,y, sN
m = estimated coordinates of a landmark
s = sensor’s signature for this landmark
Very similar to EKF localization, starting at origin

## Slide 43: EKF-SLAM
Grey: Robot Pose Estimate
White: Landmark Location Estimate

## Slide 44: Visual Slam
Single Camera
What’s harder?
How could it be possible?
Notes: angle

## Slide 45: GraphSLAM
SLAM can be interpreted as a sparse graph of nodes and constraints between nodes.

## Slide 46: GraphSLAM
SLAM can be interpreted as a sparse graph of nodes and constraints between nodes.
nodes: robot locations and map-feature locations
edges: constraints between
  consecutive robot poses (given by the odometry input u)
  robot poses and the features observed from these poses.

## Slide 47: GraphSLAM
Key property: constraints are not to be thought as rigid constraints but as soft constraints
  Constraints acting like springs
Solve full SLAM by relaxing these constraints
  get the best estimate of the robot path and the environment map by computing the state of minimal energy of this spring mass network

## Slide 48: GraphSLAM

## Slide 49: GraphSLAM

## Slide 50: GraphSLAM

## Slide 51: GraphSLAM
Build graph
Inference: solve system of linear equations to get map and path

## Slide 52: GraphSLAM
The update time of the graph is constant.
The required memory is linear in the number of features.
Final graph optimization can become computationally costly if the robot path is long.
Impressing results with even hundred million features.
Notes: End of 483_13