## Slide 2
Beyond trial and error….
Establish mathematically how robot should move
Kinematics: how robot will move given motor inputs
Inverse-kinematics: how to move motors to get robot to do what we want

## Slide 3
Robot is at (initial frame)
  xI,yI,θI
Wants to get to some
location but can’t control
  xI,yI,θI directly

## Slide 4: Robot can know
Speeds of wheels: φ1…φn
Steering angle of steerable wheels: β1…βm
Speed with which steering angles are changing:
β1…βm
These define the forward motion of the robot, the forward kinematics:
f(φ1…φn, β1…βm, β1…βm)=[xI,yI,θI]T

## Slide 5: Want we want
Reverse Kinematics
[φ1…φn, β1…βm, β1…βm] T=f(xI,yI,θI)

## Slide 6: Robot
Robot knows how it moves relative to center of rotation
Not the same as knowing how it moves in the world
Initial Frame
Robot Frame

## Slide 7
Robot Position: ξI=[xI,yI,θI]T
Mapping between frames
ξR=R(θ)ξI
=R(θ)[xI,yI,θI]T
where
R(θ)=

## Slide 9
ξR=R(θ)ξI
Still isn’t what we want… we want the reverse kinematic model
ξI=R(θ)-1ξR

## Slide 11
If we know the relative changes in x, y, and θ, we can find the global position. How do we know what these values are?

## Slide 12
Speed of the wheels
Constraints
  Movement on a horizontal plane
  Point contact of wheels
  Wheels are not deformable
  Pure rolling: velocity is 0 at contact point
  No friction for rotation
  Steering axes orthogonal to surface
  Wheels connected by rigid frame

## Slide 13: Differential Drive
Wheels rotate at φ
Each wheel contributes
rφ/2
to motion of center of rotation
Speed = sum of two wheels
Rotation due to right wheel is
ωr=rφ/2l
Counterclockwise about left wheel
l is distance between wheels

## Slide 14: Differential Drive
Rotation due to left wheel:
ωl=-rφ/2l
Counterclockwise about right wheel
Combining components:

## Slide 15: Example 1/3
θ=π/2
r=1
l=1
φl=4, φr=2
sin(π/2)=1, cos(π/2)=0

## Slide 16: Example 2/3
θ=π/4
rl=2, rr=3
l=5
φl= φr =6
sin(π/4)=1/√2, cos(π/4)=1/√2

## Slide 17: Example 3/3
A Create robot has wheels with a 5 cm radius which are 30 cm apart. Both wheels rotating clockwise at 1 rad per second. What are[xR,yR,θR]T in m/s and rad/s? What are[xI,yI,θI]T in m/s and rad/s?

## Slide 18: Sliding constraint
Standard wheel has no lateral motion
Move in circle whose center is on “zero motion line” through the axis
Instantaneous Center of Rotation

## Slide 19: More complex
Steered standard wheel
Caster wheel
More parameters

## Slide 20: Differential drive
Rotation not constrained
Can move in any circle it wants to
Easy to move around

## Slide 21: Mobile Robot Locomotion
Instantaneous center of rotation (ICR) or Instantaneous center of curvature (ICC)
  A cross point of all axes of the wheels

## Slide 22: Degree of Mobility
Degree of mobility
  The degree of freedom of the robot motion
Degree of mobility : 0
Degree of mobility : 2
Degree of mobility : 3
Degree of mobility : 1
Cannot move anywhere (No ICR)
Fixed arc motion (Only one ICR)
Variable arc motion (line of ICRs)
Fully free motion
( ICR can be located at any position)

## Slide 23: Degree of Steerability
Degree of steerability
  The number of centered orientable wheels that can be steered independently in order to steer the robot
Degree of steerability : 0
Degree of steerability : 2
Degree of steerability : 1
No centered orientable wheels
One centered orientable wheel
Two mutually dependent centered orientable wheels
Two mutually independent centered orientable wheels

## Slide 24: Degree of Maneuverability
Degree of Mobility 3 2 2 1 1
Degree of Steerability 0 0 1 1 2
The overall degrees of freedom that a robot can manipulate:
Examples of robot types (degree of mobility, degree of steerability)

## Slide 25: Degree of Maneuverability

## Slide 26: Holonomic Robots
Holonomic kinematic constraint can be expressed as explicit function of position variables only
Non-holonomic constraint requires addition information
Fixed/steered standard wheels impose non-holonomic constraints

## Slide 27: Non-holonomic constraint
So what does that mean? Your robot can move in some directions (forward
and backward), but not others (sideward)
The robot can instantly
move forward and backward,
but can not move sideward
Parallel parking,
Series of maneuvers
A non-holonomic constraint is a constraint on the feasible velocities of a body

## Slide 28: Kinematic model for car-like robot
Control Input
Driving type: Forward wheel drive
X
Y


: forward vel
: steering vel

## Slide 29: Kinematic model for car-like robot
X
Y


non-holonomic constraint:
: forward velocity
: steering velocity

## Slide 30: Dynamic Model
X
Y


Dynamic model