## Slide 1
https://www.youtube.com/watch?v=INyVbf-yG7s#t=15

## Slide 2
Robot Position: ξI=[xI,yI,θI]T
Mapping between frames
ξR=R(θ)ξI, ξI=R(θ)-1ξR
R(θ)=
Each wheel contributes to speed: rφ/2
For rotation, right wheel contributes:
ωr=rφ/2l
Notes: Nick

## Slide 3: Example
θ=π/4
rl=2, rr=3
l=5
φl= φr =6
sin(π/4)=1/√2, cos(π/4)=1/√2
1) What is ξR?
2) What is ξI?

## Slide 4
Note: Piazza post
Note: Lab 3, Lab 4, lecture

## Slide 5
There is no ideal drive configuration that simultaneously maximizes stability, maneuverability, and controllability
Example: typically inverse correlation between controllability and maneuverability

## Slide 6: Holonomicity
If the controllable degrees of freedom is equal to the total degrees of freedom then the robot is said to be holonomic.
  Holonomic constraints reduce the number of degrees of freedom of the system
If the controllable degrees of freedom are less than the total degrees of freedom it is non-holonomic
A robot is considered to be redundant if it has more controllable degrees of freedom than degrees of freedom in its task space

## Slide 7: Why study holonomic constraints?
How many independent motions can our turtlebot robot produce?
  2 at the most
How many DOF in the task space does the robot need to control?
  3 DOF
The difference implies that our system has holonomic constraints

## Slide 8
Open loop control vs. Closed loop control
Car’s cruse control

## Slide 9
Open loop control vs. Closed loop control
Recap
  Control Architectures
  Sensors & Vision
  Control & Kinematics

## Slide 10: Core AI Problem
Mobile robot path planning: identifying a trajectory that, when executed, will enable the robot to reach the goal location
Representation
  State (state space)
  Actions (operators)
  Initial and goal states
Plan:
  Sequence of actions/states that achieve desired goal state

## Slide 12
Model of the world
Compute Path
Smooth it and satisfy differential constraints
Design a feedback control law that tracks the trajectory
Design a trajectory (velocity function) along the path
Execute

## Slide 13: Fundamental Questions
How is a plan represented?
How is a plan computed?
What does the plan achieve?
How do we evaluate a plan’s quality?

## Slide 14: 1) World is known, goal is not

## Slide 15: 2) Goal is known, world is not

## Slide 16: 3) World is known, goal is known

## Slide 17: 4) Finding shortest path?

## Slide 18: 5) Finding shortest path with costs

## Slide 19: The World consists of...
Obstacles
  Places where the robot can’t (shouldn’t) go
Free Space
  Unoccupied space within the world
  Robots “might” be able to go here
    There may be unknown obstacles
    The state may be unreachable

## Slide 20: Configuration Space (C-Space)
Configuration Space: the space of all possible robot configurations.
  Data structure that allows us to represent occupied and free space in the environment

## Slide 21: Configuration Space
For a point robot moving in 2-D plane, C-space is
qgoal
qinit
C
Cfree
Cobs
Point robot (no constraints)

## Slide 22: What if the robot is not a point?

## Slide 23
Expand obstacle(s)
Reduce robot
What if the robot is not a point?

## Slide 24: What if we want to preserve the angular component?

## Slide 25: If we want to preserve the angular component…

## Slide 26: Rigid Body Planning

## Slide 27: Transfer in Reinforcement Learning via Shared Features: Konidaris, Scheidwasser, and Barto, 2012

## Slide 29: Back to Path Planning…
Typical simplifying assumptions for indoor mobile robots:
  2 DOF for representation
  robot is round, so that orientation doesn’t matter
  robot is holonomic, can move in any direction

## Slide 30: Back to Path Planning…
Now lets assume that someone gave us a map. How do we plan a path from to
How is a plan represented?
How is a plan computed?
What does the plan achieve?
How do we evaluate a plan’s quality?
Fundamental Questions
start
goal
qinit to qgoal?

## Slide 31: Discretize
start
goal

## Slide 32: Occupancy Grid
start
goal

## Slide 33: Occupancy Grid, accounting for C-Space
start
goal

## Slide 34: Occupancy Grid, accounting for C-Space
start
goal
Slightly larger grid size can make the goal unreachable.
Problem if grid is “too small”?

## Slide 35: 4) Finding shortest path

## Slide 36: General Tree Search
Important ideas:
  Fringe
  Expansion
  Exploration strategy
Main question: which fringe nodes to explore?

## Slide 37: Review: Depth First Search
S
a
b
d
p
a
c
e
p
h
f
r
q
q
c
G
a
q
e
p
h
f
r
q
q
c
G
a
S
G
d
b
p
q
c
e
h
a
f
r
q
p
h
f
d
b
a
c
e
r
Strategy: expand deepest node first
Implementation: Fringe is a LIFO stack

## Slide 38: Depth-first search
Expand deepest unexpanded node
Implementation:
  fringe = LIFO queue, i.e., put successors at front (i.e. a stack)

## Slide 39: Depth-first search
DEMOS
Notes: cd /Users/taylorm/Documents/pacman/published/demos
python pacman.py -l contoursMaze -p SearchAgent -a fn=dfs --frameTime -1
python pacman.py -p SearchAgent -a fn=dfs -l smallMaze --frameTime -1

## Slide 40: Review: Breadth First Search
S
a
b
d
p
a
c
e
p
h
f
r
q
q
c
G
a
q
e
p
h
f
r
q
q
c
G
a
S
G
d
b
p
q
c
e
h
a
f
r
Search
Tiers
Strategy: expand shallowest node first
Implementation: Fringe is a FIFO queue

## Slide 41: Breadth-first search
Expand shallowest unexpanded node
Implementation:
  Fringe is a FIFO queue, i.e., new successors go at end
DEMOS
Notes: cd /Users/taylorm/Documents/pacman/published/demos
python pacman.py -l contoursMaze -p SearchAgent -a fn=bfs --frameTime -1
python pacman.py -p SearchAgent -a fn=bfs -l smallMaze --frameTime -1

## Slide 42: DFS
Infinite paths make DFS incomplete…
How can we fix this?
Algorithm |  | Complete | Optimal | Time | Space
DFS | Depth First Search | N | N | O(BLMAX) | O(LMAX)
START
GOAL
a
b
N
N
Infinite
Infinite

## Slide 43: DFS
With cycle checking, DFS is complete.*
Algorithm |  | Complete | Optimal | Time | Space
DFS | w/ Path Checking |  |  |  | 
Y
N
O(bm+1)
O(bm)
…
b
1 node
b nodes
b2 nodes
bm nodes
m tiers
* Or with graph search version of DFS

## Slide 44: BFS
When is BFS optimal?
Algorithm |  | Complete | Optimal | Time | Space
DFS | w/ Path Checking |  |  |  | 
BFS |  |  |  |  | 
Y
N
O(bm+1)
O(bm)
…
b
1 node
b nodes
b2 nodes
bm nodes
s tiers
Y
N*
O(bs+1)
O(bs)
bs nodes

## Slide 45
In this problem the start state is S, and the goal state is G. IGNORE the heuristic estimate, h, and the transition costs next to the edges. Assume that ordering is defined by, and ties are always broken by, choosing the state that comes first alphabetically.
What is the order of states expanded using Depth First Search? Assume DFS terminates as soon as it reaches G.
What is the order of states expanded using Breadth First Search? Assume BFS terminates as soon as it reaches G.
Notes: SABDFG
SABCDEFG