## Slide 1: http://www.uasvision.com/2013/10/09/dji-phantom-crashes-into-canadian-lake/

## Slide 2: HW2
Under door by 11:59pm today
Via Angel by 11:59pm today
(or just hand it to me now)
Any questions? (Can also talk after class.)

## Slide 3
Next Monday (10/14)
  Tell Me About It: Language and Learning for Human-Robot Interaction
  4:10pm, EME 52
  Cynthia Matuszek is a Ph.D. candidate in Computer Science and Engineering at the University of Washington, studying with Drs. Dieter Fox and Luke Zettlemoyer. Her research focuses on how robots can interact robustly in unconstrained real-world settings.
Next Tuesday
  Intro to HRI
Next Thursday
  Reaction to “Camera-Based Navigation of a Low-Cost Quadrocopter”
  Review
Next next Tuesday
  Midterm
  Remember, book is in lab if you want to study

## Slide 4: Due by 11:59pm on Wednesday, 10/16
http://vision.in.tum.de/_media/spezial/bib/engel12iros.pdf
Reaction 1 paragraph to ½ a page
What did you find interesting?
What was confusing?
Summarize the paper
What questions does this paper raise?
Any ideas for a future project from this paper?

## Slide 5: Overview
Histogram Filter
  Discrete
  Multimodal
Particle Filter
  Continuous
  Multimodal
Kalman Filter
  Continuous
  Unimodal

## Slide 6: Example

## Slide 7: Example
Right

## Slide 8: Example

## Slide 9: Example
Right

## Slide 10: Kalman Filter Model
Area under the curve sums to
Gaussian
(in for now)
σ2

## Slide 11: Kalman Filter
Sense
Move
Initial Belief
Gain Information
Lose
Information
Bayes Rule
(Multiplication)
Convolution
(Addition)
Gaussian:
μ, σ2

## Slide 12: Measurement Example
Prior Position Estimate
Measurement Estimate
μ, σ2
v, r2

## Slide 13: Measurement Example
Prior Position Estimate
Measurement Estimate
Where is the new mean ?
μ, σ2
v, r2

## Slide 14: Measurement Example
Prior Position Estimate
Measurement Estimate
What is the new covarance ?
μ, σ2
v, r2
σ2’?

## Slide 15: Measurement Example
Prior Position Estimate
Measurement Estimate
New Estimate
μ, σ2
v, r2
μ', σ2’
To calculate, go through and multiply the two Gaussians and renormalize to sum to 1
Also, the multiplication of two Gaussian random variables is itself a Gaussian

## Slide 16: Multiplying Two Gaussians
(ignoring the constant term in front)
To find the mean, need to maximize this function (i.e. take derivative)
Set equal to and solve for
…something similar for the variance
Prior Position Estimate
Measurement Estimate
μ, σ2
v, r2
(ignoring constant term in front)
To find mean, maximize function (i.e., take derivative)
4. Set equal to 0 and solve for x
… something similar for the variance:

## Slide 17: Another point of view…
Prior Position Estimate
Measurement Estimate
New Estimate
μ, σ2
v, r2
μ', σ2’
: p(x)
: p(z|x)
: p(x|z)

## Slide 18: Example
Prior Position Estimate
Measurement Estimate

## Slide 19: Example
Prior Position Estimate
Measurement Estimate
Notes: Sigma2 = 16*16 / (16+16) = 256/32 = 8 -> 2.83
Q=(10*16+12*16)/)=(160+192)/32)=11

## Slide 20: Example
Prior Position Estimate
Measurement Estimate
μ’=12.4
σ2’=1.6

## Slide 21: Kalman Filter
Sense
Move
Initial Belief
Lose
Information
Convolution
(Addition)
Gaussian:
μ, σ2

## Slide 22: Motion Update
For motion
Model of motion noise
μ’=μ+u
σ2’=σ2+r2
u, r2

## Slide 23: Motion Update
For motion
Model of motion noise
μ’=μ+u
σ2’=σ2+r2
u, r2
Prior Position Estimate
M

## Slide 24: Motion Update
For motion
Model of motion noise
μ’=μ+u=18
σ2’=σ2+r2=10
u, r2
Prior Position Estimate
M

## Slide 25: Kalman Filter
Sense
Move
Initial Belief
Gaussian:
μ, σ2
μ’=μ+u=18
σ2’=σ2+r2=10

## Slide 26: Kalman Filter in Multiple Dimensions
2D Gaussian

## Slide 27: Implementing a Kalman Filter example
VERY simple model of robot movement:
What information do our sensors give us?

## Slide 28: Implementing a Kalman Filter example
H = [1 0]
F
H

## Slide 29: Implementing a Kalman Filter
estimate
P’ uncertainty covariance
state transition matrix
u motion vector
F motion noise
measurement
measurement function
measurement noise
identity matrix

## Slide 30: Summary
Kalman Filter
  Continuous
  Unimodal
  Harder to implement
  More efficient
  Requires a good starting guess of robot location
Particle Filter
  Continuous
  Multimodal
  Easier to implement
  Less efficient
  Does not require an accurate prior estimate

## Slide 32: SLAM
Simultaneous localization and mapping:
    Is it possible for a mobile robot to be placed at an unknown location in an unknown environment and for the robot to incrementally build a consistent map of this environment while simultaneously determining its location within this map?
http://flic.kr/p/9jdHrL

## Slide 33: Three Basic Steps
The robot moves
  increases the uncertainty on robot pose
  need a mathematical model for the motion
  called motion model

## Slide 34: Three Basic Steps
The robot discovers interesting features in the environment
  called landmarks
  uncertainty in the location of landmarks
  need a mathematical model to determine the position of the landmarks from sensor data
  called inverse observation model

## Slide 35: Three Basic Steps
The robot observes previously mapped landmarks
  uses them to correct both self localization and the localization of all landmarks in space
  uncertainties decrease
  need a model to predict the measurement from predicted landmark location and robot localization
  called direct observation model

## Slide 36: How to do SLAM

## Slide 37: How to do SLAM

## Slide 38: How to do SLAM

## Slide 39: How to do SLAM

## Slide 40: How to do SLAM

## Slide 41: How to do SLAM

## Slide 42: How to do SLAM

## Slide 43: How to do SLAM

## Slide 44: How to do SLAM

## Slide 45: The Essential SLAM Problem

## Slide 46: SLAM Paradigms
Some of the most important approaches to SLAM:
  Extended Kalman Filter SLAM (EKF SLAM)
  Particle Filter SLAM (FAST SLAM)
  GraphSLAM

## Slide 47: EKF Slam
Keep track of combined state vector at time t:
  x, y, θ
  m1,x, m1,y, s1
  …
  mN,x, mN,y, sN
m = estimated coordinates of a landmark
s = sensor’s signature for this landmark
Very similar to EKF localization, starting at origin

## Slide 48: EKF-SLAM
Grey: Robot Pose Estimate
White: Landmark Location Estimate

## Slide 49: Visual Slam
Single Camera
What’s harder?
How could it be possible?
Notes: angle

## Slide 50: GraphSLAM
SLAM can be interpreted as a sparse graph of nodes and constraints between nodes.

## Slide 51: GraphSLAM
SLAM can be interpreted as a sparse graph of nodes and constraints between nodes.
nodes: robot locations and map-feature locations
edges: constraints between
  consecutive robot poses (given by the odometry input u)
  robot poses and the features observed from these poses.

## Slide 52: GraphSLAM
Key property: constraints are not to be thought as rigid constraints but as soft constraints
  Constraints acting like springs
Solve full SLAM by relaxing these constraints
  get the best estimate of the robot path and the environment map by computing the state of minimal energy of this spring mass network

## Slide 53: GraphSLAM

## Slide 54: GraphSLAM

## Slide 55: GraphSLAM

## Slide 56: GraphSLAM
Build graph
Inference: solve system of linear equations to get map and path

## Slide 57
 | x1 | x2 | x3 | m1 | m2
x1 | 1 | -1 | 0 | 0 | 0
x2 | -1 | 1 | 0 | 0 | 0
x3 | 0 | 0 | 0 | 0 | 0
m1 | 0 | 0 | 0 | 0 | 0
m2 | 0 | 0 | 0 | 0 | 0
5
x1
1. The equation is changed so that both terms are grouped together and the term,
corresponding to the source pose, has positive sign:
Then, +1 and -1 coefficients are added to the matrix. The -5 constraint is added to the corresponding source pose element in the vector.
2. You do the same for the equation with positive sign for the destination pose:
Each observation (movement, sensing) adds a constraint to the matrix and vector through addition to the four elements of the matrix defined over those entities.
x2 = x1 + 5
x1 – x2 = -5
x2 - x1 = 5
-5 | 
5 | 
0 | x3
0 | 
0 | 
Ω ξ

## Slide 58
 | 1 | -1 | 0 | 0 | 0
 | -1 | 1 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0
-5 | 
5 | 
0 | 
0 | 
0 | 
5
-4
Ω ξ

## Slide 59
 | 1 | -1 | 0 | 0 | 0
 | -1 | 2 | -1 | 0 | 0
 | 0 | 2 | 1 | 0 | 0
 | 0 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0 | 0
-5 | 
9 | 
-4 | 
0 | 
0 | 
5
=9
-4
9
 | x1 | x2 | x3 | m1 | m2
x1 | 1 | -1 | 0 | 0 | 0
x2 | -1 | 2 | -1 | 0 | 0
x3 | 0 | 2 | 1 | 0 | 0
m1 | 0 | 0 | 0 | 0 | 0
m2 | 0 | 0 | 0 | 0 | 0
-5 | 
9 | 
-4 | x3
0 | 
0 | 

## Slide 60: Graph SLAM
To solve for the position of the robot and landmarks, invert and multiply by .
Ωξ

## Slide 61: Example
3 robot movements:
Resulting and :

## Slide 62: GraphSLAM
The update time of the graph is constant.
The required memory is linear in the number of features.
Final graph optimization can become computationally costly if the robot path is long.
Impressing results with even hundred million features.