## Slide 2: Communication
Piazza
  Code
Email: Angel
Computers in Lab
Joined late
  Be sure to email me to remind me!

## Slide 3
Lab 2: Questions?
  Video camera
Homework
  Coming soon
  Covering last material today & next Tue
Lab 3
  Set height
  Find marks
  Fly towards
  Land at certain distance

## Slide 4: Power vs. Attainable Speed
# of actuators
Structural complexity
Control expense
Efficiency
  Terrain
Motion of the masses
Losses

## Slide 5: Leg Configurations
A minimum DOF required to move a leg forward?

## Slide 6: Leg Configurations
A minimum of two DOF is required to move a leg forward
  a lift and a swing motion
  sliding free motion in more then only one direction not possible
Three DOF for each leg in most cases
Fourth DOF for the ankle joint
  might improve walking
  however, additional joint (DOF) increase the complexity of the design and especially of the locomotion control.

## Slide 7
“Often clever mechanical design can perform the same operations as complex active control circuitry.”

## Slide 8: Examples of 3 DOF Legs

## Slide 9: Legged Robot Control
Gait control: Leg coordination for locomotion
The gait is the sequence of lift and release events for the individual legs.
For a robot with k legs, the total number of distinct event sequences N is:
N = (2k-1)!

## Slide 10: Legged Robot Control
2 legs: N = 6
  DD, UD, DD
  DD, DU, DD
  DD, UU, DD
  UD, DU, UD, DU
  UD, UU, UD
  DU, UU, DU
6 legs: N = 11! =39,916,800

## Slide 11: Gaits

## Slide 12: Stotting (also pronking or pronging)
Quadrupeds, particularly gazelles, where they spring into the air by lifting all four feet off the ground simultaneously.
Some evidence: honest signal to predators that prey animal is not worth pursuing.
Stot is a common Scots and Geordie verb meaning “bounce” or “walk with a bounce.”
Twerk is not a valid gait.

## Slide 13: Legged Robot Control
Cost of transportation:
  How much energy a robot uses to travel a certain distance.
  Usually normalized by the robot weight
  Measured in J/N-m.

## Slide 14: Cost of Transportation

## Slide 15: Legged Robot Control
Design to better exploit the dynamics
  Natural oscillations of pendula and springs
  Dynamics of a double pendulum
  Springs can be used to store energy
  Passive dynamic walkers
    http://www.youtube.com/watch?v=WOPED7I5Lac
# of legs?
  http://www.wimp.com/thelittledog/
Model inaccuracies
  http://www.youtube.com/user/altiodaltiod?feature=watch

## Slide 17: Wheeled Mobile Robots
Most popular locomotion mechanism
Highly efficient
Simple mechanical implementation
Balancing is not usually a problem.
A suspension system is needed to allow all wheels to maintain ground contact on uneven terrain.

## Slide 18: Wheeled Mobile Robots
Focus is on
  Traction
  Stability
  Maneuverability
  Control

## Slide 19: Wheel Designs
a) Standard wheels
  2 DOF
b) Castor wheels
  2 DOF

## Slide 20: Wheel Designs
c) Swedish (Omni) wheels
  3 DOF
d) Ball or spherical wheel
  3 DOF
  Think mouse ball
  Suspension issue

## Slide 21: Wheeled Mobile Robots
Stability of a vehicle is be guaranteed with 3 wheel
  center of gravity is within the triangle with is formed by the ground contact point of the wheels.
Stability is improved by 4 and more wheels
Bigger wheels allow to overcome higher obstacles
  but they require higher torque or reductions in the gear box.
Most arrangements are non-holonomic
  require high control effort
Combining actuation and steering on one wheel makes the design complex and adds additional errors for odometry.
Notes:   however, this arrangements are hyperstatic and require a flexible suspension system.

## Slide 22: Static Stability with Two Wheels
Achieved by ensuring that the center of mass is below the wheel axis.
Or using fancy balancing

## Slide 23: Motion Control
Kinematic/dynamic model of the robot
Model of the interaction between the wheel and the ground
Definition of required motion
  Speed control
  Position control
Control law that satisfies the requirements

## Slide 24: Mobile Robot Kinematics
Description of mechanical behavior of the robot for design and control
Similar to robot manipulator kinematics
However, mobile robots can move unbound with respect to their environment:
  There is no direct way to measure robot’s position
  Position must be integrated over time
  Leads to inaccuracies of the position (motion) estimate
Understanding mobile robot motion starts with understanding wheel constraints placed on the robot’s mobility

## Slide 25
Configuration: complete specification of the position of every point of the system. Position and orientation. Also, called a pose
Configuration space: space of all possible configurations
Workspace: the 2D or 3D ambient space the robot is in.

## Slide 28: Kinematics
Borrowing slides from a related course at Brooklyn College (will also be on website).