## Slide 2: Locomotion: Chapter 1
Enabling robots to move
Many bio-inspired methods:
  Walk, jump, run, slide, skate, swim, fly, roll
  Exception: Powered wheel
    Human invention
    What’s the benefit?

## Slide 3: Power vs. Attainable Speed
# of actuators
Structural complexity
Control expense
Efficiency
  Terrain
Motion of the masses
Losses

## Slide 4: Key Issues for Locomotion
Stability
  number and geometry of contact points
  center of gravity
  static/dynamic stability
  inclination of terrain

## Slide 5: Key Issues for Locomotion
Characteristics of contact
  contact point/path size and shape
  angle of contact
  friction

## Slide 6: Key Issues for Locomotion
Type of environment
  structure
  medium
    water
    air
    soft or hard ground

## Slide 7: Legged Mobile Robots
Characterized by a series of point contacts between the robot and the ground.
Adaptability and maneuverability in rough terrain
Power and mechanical complexity
High degrees of freedom
Control system complexity
http://www.youtube.com/watch?v=xlOwk6_xpWo

## Slide 8: AtlasProto by Boston Dynamics
The Atlas robots participated in the DARPA Robotics Challenge in 2013
http://www.youtube.com/watch?v=w40e1u0T1yg

## Slide 9: Leg Configurations
Minimum DOF required to move a leg forward?

## Slide 10: Leg Configurations
A minimum of two DOF is required to move a leg forward
  a lift and a swing motion
Three DOF for each leg in most cases
Fourth DOF for the ankle joint
  might improve walking
  additional joint (DOF) increase complexity of design and locomotion control

## Slide 11
“Often clever mechanical design can perform the same operations as complex active control circuitry.”

## Slide 12: Examples of 3 DOF Legs

## Slide 13: Legged Robot Control
Gait control: Leg coordination for locomotion
The gait is the sequence of lift and release events for the individual legs.
For a robot with k legs, the total number of distinct event sequences N is:
N = (2k-1)!

## Slide 14: Legged Robot Control
2 legs: N = 6
  DD, UD, DD
  DD, DU, DD
  DD, UU, DD
  UD, DU, UD, DU
  UD, UU, UD
  DU, UU, DU
6 legs: N = 11! =39,916,800

## Slide 15: Gaits

## Slide 16: Stotting (also pronking or pronging)
Quadrupeds, particularly gazelles, where they spring into the air by lifting all four feet off the ground simultaneously
Some evidence: honest signal to predators that prey animal is not worth pursuing
Stot is a common Scots and Geordie verb meaning “bounce” or “walk with a bounce”
Twerk is not a valid gait

## Slide 17: Legged Robot Control
Cost of transportation:
  How much energy a robot uses to travel a certain distance
  Usually normalized by the robot weight
  Measured in J/N-m

## Slide 18: Cost of Transportation

## Slide 19: Legged Robot Control
Design to better exploit the dynamics
  Natural oscillations of pendula and springs
  Dynamics of a double pendulum
  Springs can be used to store energy
  Passive dynamic walkers
    http://www.youtube.com/watch?v=WOPED7I5Lac
# of legs?
  http://www.wimp.com/thelittledog/
Model inaccuracies
  http://www.youtube.com/user/altiodaltiod?feature=watch

## Slide 20: Wheeled Mobile Robots
Most popular locomotion mechanism
Highly efficient
Simple mechanical implementation
Balancing is not usually a problem
Suspension system needed to allow all wheels to maintain ground contact on uneven terrain

## Slide 21: Wheeled Mobile Robots
Focus is on
  Traction
  Stability
  Maneuverability
  Control

## Slide 22: Wheel Designs
a) Standard wheels
  2 DOF
b) Castor wheels
  2 DOF

## Slide 23: Wheel Designs
c) Swedish (Omni) wheels
  3 DOF
d) Ball or spherical wheel
  3 DOF
  Think mouse ball
  Suspension issue

## Slide 24: Wheeled Mobile Robots
Stability of a vehicle is guaranteed with 3 wheel
  center of gravity is within the triangle with is formed by the ground contact point of wheels
Stability is improved by 4 and more wheels
Bigger wheels allow to overcome higher obstacles
  But require higher torque or reductions in the gear box
Most arrangements are non-holonomic
  require high control effort
Combining actuation and steering on one wheel makes design complex and adds additional errors for odometry
Notes:   however, this arrangements are hyperstatic and require a flexible suspension system.

## Slide 25: Static Stability with Two Wheels
Achieved by ensuring center of mass is below wheel axis
Or using fancy balancing

## Slide 26: Motion Control
Kinematic/dynamic model of the robot
Model the interaction between wheel and ground
Definition of required motion
  Speed control
  Position control
Control law that satisfies the requirements

## Slide 27: Mobile Robot Kinematics
Description of mechanical behavior of the robot for design and control
Similar to robot manipulator kinematics
However, mobile robots can move unbound with respect to their environment:
  No direct way to measure robot’s position
  Position must be integrated over time
  Leads to inaccuracies of the position (motion) estimate
Understanding mobile robot motion starts with understanding wheel constraints placed on robot’s mobility

## Slide 28
Configuration: complete specification of the position of every point of the system. Position and orientation. Also, called a pose
Configuration space: space of all possible configurations
Workspace: the 2D or 3D ambient space the robot is in.