## Slide 1
Lab 2: Questions / comments?

## Slide 2: So Far…
Compass
Wheel encoders
Gyroscope
  v.s. Accelerometer?
GPS
  Beacons
  Sound
  WiFi
  Etc.
Notes: Gyroscope = orientation
Non-rotational. Crystals get stressed under movement, causing voltage
Quantified Self movement
Iphone = accelerometer + compass

## Slide 3: Range Sensors (time of flight) (1)
Large range distance measurement: range sensors
Range information:
  key element for localization and environment modeling
  Ultrasonic sensors: Sound
  Laser sensors: electromagnetic waves
Notes:   Distance = speed * time

## Slide 4: Range Sensors (time of flight) (2)
Propagation speed v of sound: 0.3 m/ms
Propagation speed v of of electromagnetic signals: 0.3 m/ns, one million times faster
time of flight t with electromagnetic signals is not an easy task
  laser range sensors expensive and delicate
Quality of time of flight range sensors manly depends on:
  Uncertainties about the exact time of arrival of the reflected signal
  Inaccuracies in the time of fight measure (laser range sensors)
  Opening angle of transmitted beam (ultrasonic range sensors)
  Interaction with the target (surface, specular reflections)
  Variation of propagation speed
  Speed of mobile robot and target (if not at standstill)

## Slide 5: Ultrasonic Sensor (1)
Transmit packet of (ultrasonic) pressure waves
Distance d of the echoing object can be calculated based on the propagation speed of sound c and the time of flight t
The speed of sound c (340 m/s) in air is given by
where
: ratio of specific heats
R: gas constant
T: temperature in degree Kelvin
Notes: D = ct/2
C = sqrt(gamma * R * T)

## Slide 6: Ultrasonic Sensor (2)
time
Analog
Signal
time
Threshold
time
Integrated
Input

## Slide 7: Ultrasonic Sensor (3)
Transmitted sound
Analog echo signal
Threshold
Digital echo signal
Integrated time
Output signal
integrator
Time of flight (sensor output)
threshold
Wave packet
Threshold: high initially (avoid ringing) then decreases over time
Very close objects = trouble!

## Slide 8: Ultrasonic Sensor (4)
typically a frequency 40 - 180 kHz
generation of sound wave: piezoelectric transducer
  Early application: WWI sonar
sound beam propagates in a cone-like manner
  opening angles around 20 to 40 degrees
  segments of an arc (sphere for 3D)
  Typical intensity distribution of a ultrasonic sensor

## Slide 9: Ultrasonic Sensor (5)
Soft surfaces that absorb most of the sound energy
Surfaces far from perpendicular to the direction of sound: specular reflection
360° scan

## Slide 10: Speed of Light
Fizeau apparatus

## Slide 11: Speed of Light
Fizeau apparatus

## Slide 12: Speed of Light
Fizeau apparatus
Foucault apparatus

## Slide 13: Laser Range Sensor (1)
Transmitted and received beams coaxial
Transmitter illuminates a target with a collimated beam
Received detects the time needed for round-trip
A mechanical mechanism with a mirror sweeps
  2 or 3D measurement
Notes: Laser
D
Target

## Slide 14: Laser Range Sensor (2)
Pulsed laser
  measurement of elapsed time directly
Beat frequency
  between a frequency modulated continuous wave and received reflection

## Slide 15: Laser Range Sensor (3)
Phase-Shift Measurement (easier than other 2 methods)
c: speed of light; f: modulating frequency, θ: phase measurement
  for f = 5 Mhz, l = 60 meters
l = c/f

## Slide 16: Laser Range Sensor (4)
Distance D, between the beam splitter and the target
: phase difference between the transmitted
Theoretically ambiguous range estimates
  since for example if  = 60 meters, a target at a range of 5 meters = target at 35 meters

## Slide 17: Example Laser Range Sensor
Length of lines through the measurement points indicate the uncertainties
http://www.youtube.com/watch?v=NC1F0TwJ_Q8

## Slide 18: Structured Light Projection
What if you projected a pattern instead of a point. How would this be useful?

## Slide 19: Structured Light Projection
What if you projected a pattern instead of a point. How would this be useful?

## Slide 20: Triangulation Ranging
Geometrical properties of image establish a distance measurement
Project a well defined light pattern (e.g. point, line) onto the environment
  Reflected light captured by a photo-sensitive line or matrix (camera) sensor device
  Triangulation establishes distance

## Slide 21: Laser Triangulation (1D)
  Principle of 1D laser triangulation.
  distance is proportional to the 1/x
Target
D
L
Laser / Collimated beam
Transmitted Beam
Reflected Beam
P
Position-Sensitive Device (PSD)
or Linear Camera
x
Lens

## Slide 22: Structured Light (vision, 2 or 3D)
Eliminate correspondence problem by projecting structured light on the scene
Slits of light / emit collimated light (laser) by means of rotating mirror
Light perceived by camera
Range to an illuminated point can then be determined from simple geometry.
u

## Slide 23: Structured Light (vision, 2 or 3D)
Eliminate correspondence problem by projecting structured light on the scene
Slits of light / emit collimated light (laser) by means of rotating mirror
Light perceived by camera
Range to an illuminated point can then be determined from simple geometry.
u

## Slide 24: Doppler Effect Based (Radar or Sound)
a) between two moving objects b) between a moving and a stationary object
transmitter is moving receiver is moving
Doppler frequency shift relative speed

## Slide 26: Locomotion: Chapter 1
Enabling robots to move
Many bio-inspired methods:
  Walk, jump, run, slide, skate, swim, fly, roll
  Exception: Powered wheel
    Human invention
    What’s the benefit?

## Slide 27: Power vs. Attainable Speed
# of actuators
Structural complexity
Control expense
Efficiency
  Terrain
Motion of the masses
Losses

## Slide 28: Key Issues for Locomotion
Stability
  number and geometry of contact points
  center of gravity
  static/dynamic stability
  inclination of terrain

## Slide 29: Key Issues for Locomotion
Characteristics of contact
  contact point/path size and shape
  angle of contact
  friction

## Slide 30: Key Issues for Locomotion
Type of environment
  structure
  medium
    water
    air
    soft or hard ground

## Slide 31: Legged Mobile Robots
Characterized by a series of point contacts between the robot and the ground.
Adaptability and maneuverability in rough terrain
Power and mechanical complexity
High degrees of freedom
Control system complexity

## Slide 33: DarDARPA Robotics Challenge (2015)

## Slide 34: Leg Configurations
What is a DOF?
Minimum DOF required to move a leg forward?

## Slide 35: Leg Configurations
A minimum of two DOF is required to move a leg forward
  a lift and a swing motion
Three DOF for each leg in most cases
Fourth DOF for the ankle joint
  might improve walking
  additional joint (DOF) increase complexity of design and locomotion control

## Slide 36
“Often clever mechanical design can perform the same operations as complex active control circuitry”

## Slide 37: Examples of 3 DOF Legs

## Slide 38: Legged Robot Control
Gait control: Leg coordination for locomotion
The gait is the sequence of lift and release events for the individual legs.
For a robot with k legs, the total number of distinct event sequences N is:
N = (2k-1)!

## Slide 39: Legged Robot Control
2 legs: N = 6
  DD, UD, DD
  DD, DU, DD
  DD, UU, DD
  UD, DU, UD, DU
  UD, UU, UD
  DU, UU, DU

## Slide 40: Legged Robot Control
2 legs: N = 6
  DD, UD, DD
  DD, DU, DD
  DD, UU, DD
  UD, DU, UD, DU
  UD, UU, UD
  DU, UU, DU
6 legs: N = 11! =39,916,800

## Slide 41: Gaits

## Slide 42: Stotting (also pronking or pronging)
Quadrupeds, particularly gazelles, where they spring into the air by lifting all four feet off the ground simultaneously
Some evidence: honest signal to predators that prey animal is not worth pursuing
Stot is a common Scots and Geordie verb meaning “bounce” or “walk with a bounce”

## Slide 43: Legged Robot Control
Cost of transportation:
  How much energy a robot uses to travel a certain distance
  Usually normalized by the robot weight
  Measured in J/N-m

## Slide 44: Cost of Transportation

## Slide 45: Legged Robot Control
Design to better exploit the dynamics
  Natural oscillations of pendula and springs
  Dynamics of a double pendulum
  Springs can be used to store energy
  Passive dynamic walkers
    http://www.youtube.com/watch?v=WOPED7I5Lac
# of legs?
  http://www.wimp.com/thelittledog/
Model inaccuracies
  http://www.youtube.com/user/altiodaltiod?feature=watch