## Slide 1
Environmental Innovation Challenge
  Funding deadline soon
  Travel funds available too
Business Plan Competition
  Late Spring
  Interdisciplinary is key

## Slide 2
Planetary Resources
  Projects
  Continual learning
  Changing the world

## Slide 3
Final Project
Final exam

## Slide 4
Today: Time to work on Lab 4
Next Tuesday: Lecture
Next Thursday: Matt out of town (time to work on lab 4)

## Slide 5: Lab 4
Create a new package
Create a new C++ or Python node called lab4
Set up your node to publish Twist messages to the cmd_vel_mux/input/teleop topic. Check out the turtlebot_teleop package for examples.
Implement two functions:
  publishTwist(u,w): takes in linear and angular velocity as inputs and publishes to robot
  spinWheels (u1, u2, time): takes in velocities of left and right wheels and drives the robot for the specified period of time.
Modify your node to subscribe to Odometry messages. Check out turtlebot/src/kobuki/kobuki_node for examples.
Implement two functions:
  driveStraight(speed, distance) : should be in m/s and m
  rotate(angle) : can be degrees or radians
Finally, write an executeTrajectory() function that will
  Drive the turtlebot in a square pattern with 50cm sides
  Drive the turtlebot in an equilateral triangle pattern with 25 cm sides
Turn in (11:59pm on 11/17): brief writeup, code, video
Suggestions:
  You can run everything on the netbook for this lab, if you want
  Don’t forget about the ROS Tutorials
  I recommend you work in teams, but it’s not required
  Post questions to Piazza